## Slide 1: Capacity Planning and Optimization
ELEC 457
Ben Wilkinson

## Slide 2: What is capacity planning?
Forecasting Demand
  What are the expected energy and capacity requirements in 5, 10, and 15 years? Capacity (MW) and Energy (MWh) both need to be considered
Optimizing Generation Mix
  Gas generators, Solar, Wind, Hydro, Batteries, etc. for capital cost, fuel and operating risk, and project life
Infrastructure Upgrade Requirements
Meeting Environmental Goals
  Low or zero carbon emissions
Mitigating Risks
  Unable to supply the required demand
  Increased and unexpected costs

## Slide 3: Optimization Software Choice
PyPSA used as optimization tool for capacity planning
  Provides extensive documentation and examples for users
  Built to model and optimize many different power systems efficiently
  Compatible with plenty of solvers (GLPK, highs, pyomo, etc.)
  Electrical objective and constraint equations built into the package

## Slide 4: Objective function
Simply put, meet the required capacity at the minimum costs, including capital, variable and fixed costs, and environmental compliance costs
The actual objective equation
  +
  The objective function is composed of capital cost c for each component and operation cost o for generation tech.
  represents the weighting of time in the objective
  is the nominal power of generator s at bus n
  In the capacity planning model, many of the terms above become zero

## Slide 5: Constraints
Don’t overload your equipment that you paid millions or maybe billions for…
Generator limits (wind, solar, OCGT, nuclear, etc.)
Storage limits (battery, hydrogen, pumped hydro, etc.)
Line limits
Capacity expansion limits (generators, storage, line capacity)

## Slide 6: The Inputs
Onshore wind and solar capacity factors data collected from model.energy
  2011 – 2014 data is available
  Selected Washington State as location due to proximity to BC
  Hourly resolution
Load data from BC Hydro Historical Transmission Data – Gross Telemetered Load
  BC Hydro Data
  2014 used as the basis for Load Data
  Hourly resolution
Technology data provided by PyPSA from GitHub
  Includes VOM, FOM, Investment, CO2 Intensity and many other data points for hundreds of technologies
  Data is available for 2030 through 2050 in 5 years increments

## Slide 7: Generators and Storage Considered
Generation Technologies
  OCGT – Open Cycle Gas Turbines
  Hydroelectricity
  Nuclear
  Wind
  Solar
Storage Technologies
  Pumped Hydro
  Battery Storage

## Slide 8: Scenarios – What can we change
Load
Investment Cost
Fuel Cost
Carbon Cost
Generation
  Types of generation available
  Maximum or minimum amount of nominal power acceptable in solution
CO2 emissions limits

## Slide 9: Scenario 1 - Year 2030
Nuclear and Hydro Available
Carbon market is available, but the cost of carbon is $150 CAD / tonne CO2e*
*CO2e is CO2-equivalent GHG
Can build as much wind and solar as we want, but we must have a 1-1 ratio with energy storage
Power increases 2% year-over-year

## Slide 10: Scenario 1 - Year 2030

## Slide 11: Scenario 1 - Year 2030
Capacities :
OCGT– 6891 MW
Onwind – 10646 MW
Solar – 40648 MW
Battery Storage – 31722 MW
System Cost:
$17.4 billion CAD

## Slide 12: Scenario 2 – Year 2040
Nuclear and Hydro Available
Carbon market is available, but the cost of carbon is $500 CAD / tonne CO2e*
*CO2e is CO2-equivalent GHG
Can build as much wind and solar as we want, but we must have a 1-1 ratio with energy storage
Power increases 2% year-over-year

## Slide 13: Scenario 2 – Year 2040

## Slide 14: Scenario 2 – Year 2040
Capacities :
OCGT– 7307 MW
Onwind – 18649 MW
Solar – 64882 MW
Battery Storage – 31802 MW
System Cost:
$20.5 billion CAD

## Slide 15: Scenario 3 – Year 2050
Nuclear and Hydro Available
Carbon emissions must be zero
Can build as much wind and solar as we want – energy storage constraint is relaxed
Power increases 2% year-over-year

## Slide 16: Scenario 3 – Year 2050

## Slide 17: Scenario 3 – Year 2050
Capacities :
Nuclear– 9630 MW
Onwind – 8981 MW
Solar – 43147 MW
Battery Storage – 45436 MW
System Cost:
$28.5 billion CAD

## Slide 18: In-class demo

## Slide 19: Proposed Model Revisions
Increase the accuracy of data
  Load data, for instance, can be difficult to forecast but is critical to get right when planning capacity
  Technology data – investment cost, lifetime, RoR, efficiency, etc.
Markets and regulation
  Changes to the energy market or regulatory environment and their effects
Stochastics
  Account for random variance in one or more parameters over time
Hourly dispatch to account for reliability and Effective Load Carrying Capacity (ELCC) of various technologies to ensure cost-effective reliable supply while accounting for variable nature of solar and wind resources
Transmission
  Capacity limits, cost of new infrastructure and losses

## Slide 20: Thanks for listening